## Slide 1: 5G New Radio: Next Generation Radio Access Network
Olalekan Peter Adare
&
Haitham Babbili
Wireless Network (SSY145)
2020-May-20

## Slide 2: Content
Introduction
Background and New Challenges
5G NR
5G Standardization and Specifications
5G NR Requirements
5G NR Design
5G NR Services
Spectrum Allocation in 5G NR
5G NR and 4G LTE Coexistence
Benefits of 5G NR
Conclusion
5G NR

## Slide 3: Introduction: What is 5G NR?
In mobile communication, the air interface is the frequency link between UE and base station in mobile communication
5G New Radio (NR) is access air interface of the 5G Network
An OFDM-based, unified, and more capable air interface
It will offer varying services, use cases, deployment scenarios and diverse spectrum
Possibility of operating from low to very high frequency bands: 0.4 - 100GHz
It will interwork with 4G LTE and Wi-fi for seamless user experience
5G NR
…
…
…
gNodeB
5G NR

## Slide 4: Background & New Challenges
1980
1G: 1980 only Analog voice
1990
2G: 1990 Digital voice and data
2000
3G: WCDMA/CDMA2000/EV-DO
voice, video and data, upgraded to 3.5G by HSPA+
2010
4G: 2010 high data rate for downlink and uplink and better coverage (100Mbps)
Ultra-high data rates
(> 1Gbps)
Ultra-large Connections (>1million)
Ultra-low latency
(<1ms)
Challenges
Network Evolution is needed to fulfill these requirement  5G NR

## Slide 5: 5G NR: Scaled for diverse uses
mMTC
URLLC
eMBB
5G NR
.
eMBB
Enhanced Mobile Broadband
URLLC
Ultra-reliable and Low-latency
Communications
mMTC
Massive Machine Type
Communication
Ultra-low latency < 1ms
Highly reliable (99.999%)
Highly secured
Ultra-high density
1million/square-Km
Optimized IoT
Low-power and low-complexity
Extreme data rate, 10Gbps peak
Extreme capacity/traffic volume
Tbps/square-Km
5G NR
Notes: Radio access technology developed by 3GPP to be global stander for air interface of 5G network
Major part
  eMBB facilitates people to people exchange
    focuses on both larger and flexible bandwidth than
    Improvement and increase data rate by increase modulation or bandwidth
  mMTC or IoT
  URLLC support services need very high reliability and low latency like remote driving
    Key for it ultra lean design and OFDM
5G NR operate at 6 GHz with bandwidth 100MHz or 24.25GHz with 400MHz band
1Gbps, 1ms, 1 million m2
5G NR spectrum improve x5 to x15 than 4G
5G cost efficiency x100 than 4G

## Slide 6: 5G Standardization and Specifications
3GPP Release 15 in 2018 gave the basic requirements for 5G NR. This became the baseline for Releases 16 and 17.
3GPP proposed practical deployment scenarios
Non-Standalone (NSA) : 5G NR relies on 4G LTE network for its control/signaling information. Data access is handled by the 5G NR network
Intended for earlier commercial use and smooth upgrade to full 5G network
Standalone (SA) : This is 5G without 4G LTE.
Here, data, control/signaling are handled end-to-end by the 5G network
5G NR

## Slide 7: 5G NR Requirements
High data rate in the order of ~Gbps
Increased bandwidth efficiency
Support for many new use cases
Support for large number of device connection
Latency of 1ms, or less
Energy efficiency and battery lifespan optimization
Scalable and customizable network
……….
5G NR

## Slide 8: 5G NR Design
Basically, to increase data rate, there should be an increase in bandwidth and the modulation schemes.
Key Design Parameters are:
Flexibility : use wide range of frequencies, deploys different technologies and depends on the physical layer components (gNB, 5GC)
  Technology: high order modulation, massive MIMO with flexible channel state information, variable numerologies, and frame structure timing sequence
Ultra lean design: reduce the ”always-on” reference signals
  Improve power efficiency
  Reduce network operator expenses
  Reduce interference in high traffic load situation
  Reduced number of reference signals since beamforming is being used
Forward compatibility: 5G NR must support a wide range of use cases, (V2V,D2D, AR,VR…) and some new cases are under review. This means it must offer support for future wireless access technologies
5G NR

## Slide 9: 5G NR Services
eMBB:
Service in 5G NR that require high data rate like high resolution video, virtual and augmented reality, and live steaming.
Depends on the physical layer: The various technologies at the layer are high modulation orders, high bandwidth, carrier aggregation, cell densification, massive MIMO, mmWave and spectral localization
mMTC:
support higher volume of IoT for services like smart city, tracking and sensing
Requires high connection density, better power efficiency and longer battery lifespan
Narrowband internet of things (NB-IoT) is a good fit mMTC. It also helps to manage the possibility of having more mMTC devices than the network can initially support.
URLLC:
services that are latency-sensitive and highly reliable. (<1ms & 99.999%) e.g. remote driving
Requires QoS priority different from that of the mobile broadband service. It is given a higher QoS priority than normal mobile services
Achieved by reducing system over-head in terms of channel access, user schedule, allocation of resources, grant-free based uplink transmission, and advanced channel coding schemes.
5G NR

## Slide 10: Spectrum Allocation in 5G NR
Frequency bands for 5G NR are separated into two different frequency ranges.
  FR1: sub 6GHz (450MHz – 6GHz) : wider coverage, lower bandwidth (100MHz)
  FR2: 24.5GHz to 52.5GHz: shorter coverage but higher bandwidth (400MHz)
5G NR use compensation of FR1 and FR2 which mean better coverage and high bandwidth
5G NR spectrum use license , unlicensed, and shared spectrum
5G NR uses both TDD and FDD as duplex technology:
  Dynamic TDD, used mostly in FR2 range. TDD and FDD is used in FR1 range.
  Self-contain structure is faster switching time
  Better spectrum utilization and guaranteed bandwidth
5G NR
6 GHz
FR2
High-frequency band, e.g mmWave
FR1
Shared with other technologies
100 GHz
0.4 GHz
24.5 GHz

## Slide 11: 5G NR and 4G Coexistence
Frequency spectrum is limited so the system needs to utilize it in an efficient way, by sharing the spectrum.
Static Sharing: good for user but not for spectrum efficient
Dynamic Sharing(DSS): based on flexible design of the physical layer
DSS minimizes the collision between 5G and 4G technologies
Coexistence between 4G and 5G can be consider as flexible re-farming
5G NR

## Slide 12: Benefits of 5G NR
More data rate per user (peak 10 Gbps)
Hyper-densification (1m/square-km)
Increased capacity and network coverage
Optimized for IoT
More reliable and low latency system e.g. mission-critical services like remote driving, sensing, telemedicine, tracking etc.
New Intelligent interconnection of devices e.g. V2X, D2D etc
5G NR

## Slide 13: Conclusion
5G NR is the access air-interface for the 5G network
5G NR focuses on eMBB, mMTC and URLLC services
The key technologies include spectrum flexibility, ultra lean design, carrier aggregation, advanced coding and massive MIMO.
5G NR can co-exist with 4G LTE seamlessly
5G NR offers better coverage for mobile services in urban, suburban and rural areas.
5G NR is the foundation for future mobile communication technologies.
5G NR

## Slide 14
THANK YOU
5G NR
Olalekan Peter Adare & Haitham Babbili